## Slide 1: Definition and implementation of a BIM integrated fully reproducible workflow for the computation of vulnerability functions of URM buildings
Midterm presentation
https://epfl.zoom.us/j/4152740646

## Slide 2: Content
1. Literature review summary
2. Case study presentation
3. BIM modeling
4. Transfer to FE application and interoperability
5. Capacity determination using EFM through SAMUEL
6. Peak demand and OSR verification
7. Building models database
8. Next steps

## Slide 3: 1. Literature review
BIM modeling of URM buildings
  URM buildings context
  BIM, important notions
  Modeling URM in BIM
BIM databases of buildings as input for FE models
  Data management in BIM
  Interoperability between BIM and FE applications
  The concept of BIM database
Equivalent frame models (EFM) of URM buildings
  Seismic behavior of URM buildings
  Description of the EFM method

## Slide 4: URM buildings context
Important part of the ageing (historical) building stock
Most vulnerable to earthquake in comparison with other types of structures
Correct earthquake resistance assessment is important from an economical and socio-cultural point of view
URM behavior is highly dependent on the building masonry and floors typology
@ European Macro-seismic scale, 1998

## Slide 5: Important BIM notions
Building Information Modeling: geometry + property data
Level of detail (LOD)
  100: Symbolic representation
  200: Generic, approximate placeholder
  300: Specific (quantity, geometry etc.)
  350: Specific + supports and connections
  400: Sufficient details for fabrication
  500: Field verified representation
OpenBIM: File exchange and file conversion are supported (by opposition with ClosedBIM)
@BIMforum

## Slide 6: Modeling URM in BIM
Most software fully support masonry modeling only until LOD 300
  Work arounds are generally needed for modeling connections
@BIMforum

## Slide 7: Data management in BIM
Exchange format: Industry foundation classes (IFC)
  ISO 16739:2013 standardized
  Exchange of 3D geometry and property
  data (not intended for 2D views)
  Different versions (IFC 4, IFC 2x3 etc.)
Model view definition (MVD)
  Based on the use
  Structural application
    Design transfer view
    Analytical model is key
@Autodesk

## Slide 8: Transfer to FE application and interoperability
Transfer of IFC file described precedingly
Level of interoperability highly depends on software
  FreeCAD ( Opensource parametric modeler used by SAMUEL)
    Level of interoperability does not permit FE applications yet (IfcOpenShell unfunctional)
BuildingSMART certification (by IFC version)
  Ensures a good level of interoperability

## Slide 9: BIM database concept
CAD models database: Mechanical engineering roots (since 1984)
  aero-spatial, automotive industry, 3D printing technology etc.
  e.g. grabcad.com (community driven sharing platform)
Finite element models database for structures design automation
  Idea originated for offshore marine structures
    Nader Shebini 1989 patent in USA for McDermott Engineering
Coupling the idea with BIM
  Powerful given the widespread and increasing usage by AEC industry
  First step for full automation of structural design (AI, machine learning…)
  AI based generative design of structures implementation has already begun
    e.g. Autodesk Revit Generative design

## Slide 10: Seismic behavior of URM buildings
2 principal failure mechanisms
  In-plane
  Out of plane (OOP)
Elastic-plastic behavior
  In-plane OOP
@ Civil 522 EPFL

## Slide 11: EFM analysis
Decomposition of an URM building’s walls into piers (in red) and spandrels (in blue), connected by rigid nodes (in grey), thus making sets of equivalent frames
Masonry piers behaves like precedingly described (elastic-plastic in-plane and OOP)
Masonry spandrels behave like beams
@github.com/eesd-epfl/OpenSees/wiki

## Slide 12: 2. Case study presentation
Typology
3D views
2D geometric survey plans

## Slide 13: Typology
General characteristics:
  Address: Basel Switzerland
  Office building: commercial and administration usage
  Year of construction: 1901
  Number of storeys: 3 without counting basement and attic
  Construction volume: 7098 m3
  Floor boundary area: 340 m2
  Assured value: 8 mio CHF
Structural characteristics:
  Massive stone masonry shell (exterior and some interior walls)
  Timber wood floor slabs
  Pitched timber roof
  Even more massive stone masonry wall foundations

## Slide 14: 3D view: Google streetview

## Slide 15: 3D views: Swisstopo (Aerial and buildings3D)

## Slide 16: 2D survey: Ground floor

## Slide 17: 2D survey: Cut

## Slide 18: 3. BIM modeling
LOD 200
LOD 300
Using Revit
GUI based workflows shared

## Slide 19: LOD 200, 3D
3D physical
3D analytical

## Slide 20: LOD 200, 2D Ground floor
2D Physical
2D Analytical

## Slide 21: LOD 200, Cut
Cut Physical
Cut Analytical

## Slide 22: LOD 300, 3D
3D physical
3D analytical

## Slide 23: LOD 300, 2D Ground floor
2D Physical
2D Analytical

## Slide 24: LOD 300, Cut
Cut Physical
Cut Analytical

## Slide 25: 4. Transfer to FE application and interoperability
Transfer from BIM to SAMUEL for EFM application is not possible yet
Interoperability issue has to do with FreeCAD 0.19 IFC processing tool, IfcOpenShell which only permit vizualisation
Workaround solution: Use the FreeCAD generated model by T.A. Ivana Bozulic

## Slide 26: 5. Capacity determination using SAMUEL
Structural model
Pushover analysis
Analysis results
Conditions

## Slide 27: Structural model
Spatial structural model
containing principal structural
members
  Principal walls (with openings)
  Floors diaphragms
Semi-automated EFM mesh
generation through SAMUEL’s
Python opensource code

## Slide 28: Pushover analysis
Displacements imposed on the control node
Iterative procedure to solve differential
equations based on the theory presented at
the literature review
Considers self-weight through simultaneous analysis
Result is a force-displacement relationship of
the structure
Visualization of the global behavior is also possible

## Slide 29: Analysis results
Analysis type |  |  |  | 
Pushover, rect |  |  |  | 
Note: All values are absolute |  |  |  | 
 | Displacements |  | Forces | 
Units | mm |  | kN | 
Direction, sense | V_peak | d_peak | 80% V_peak | d_ult
X, positive | 6311.46 | 45.12 | 5049.17 | 81.20
X, negative | 6678.45 | 37.70 | 5342.76 | 78.70
Y, positive | 6148.03 | 44.03 | 4918.42 | 371.73
Y, negative | 7105.13 | 53.15 | 5684.11 | 136.77
V_peak
d_peak
V_ult = 80% V_peak
d_ult
Eurocode 8-3: Confidence factor (See conditions next)
CF(KL1) = 1.35
C_d= d_ult/CF
C_d = 58 mm
In plane behavior (C.N.)
Ultimate deformation capacity design value

## Slide 30: Global behavior visualization
High concentration of drifts and shear damage at the ground floor
Measures should be taken to assure sufficient ductility at this level for the analysis to make sense (see conditions next)
  Soft-storey mechanism must be avoided !
Total drift
Shear damage
OOP displacement
OOP behavior (C.N.)

## Slide 31: Conditions
Knowledge level
  Geometry
    Survey of structural &
    nonstructural elements
  Material
    NDT & DT
  Detailing
(EC8 does not recommend pushover at KL1)
Details to be checked – particularly around ground floor (non exhaustive):
  Mortar joints quality and condition
  Type and condition of orthogonal walls connections
  Type and condition of floor-to-wall connections
Second analysis recommended - e.g. triangular distribution of forces
  deformation capacity tends to be similar for short buildings, @Akbas 2003
@ Eurocode 8 part 3

## Slide 32: 6. Peak demand and OSR verification
Elastic response spectrum
  Soil categorization
  Other parameters
Design response spectrum
Fundamental period and peak demand
Overstrength ratio
Assessment and recommendations

## Slide 33: Soil categorization
Online documentation
https://map.geo.admin.ch/
Gravel alluvium
https://www.geopotenziale.org/
Shallow Plio-Quaternary
unconsolidated alluvium layer over
a deep Tertiary layer of indurated
marl or sandstone
Soil is probably class A (or E depending
on the alluvium layer width – >5m)
Further geotechnical investigation should be performed to confirm

## Slide 34: Elastic response spectrum calculation
SIA 261 formula 
Ground acceleration
  SIA 261: Basel is in zone 2
Soil dependent parameters
  SIA 261 
Damping ratio
  For damaged stone masonry it could go
  down to 3% (Elmenshawi et al. 2010)

## Slide 35: Elastic response spectrums result
Acceleration
Displacement

## Slide 36: Design spectrum
uel = displacement of the elastic system for the forces from the elastic spectrum
For URM structure:
We choose a conservative value of q = 2.0 given the possible effort concentration at ground floor

## Slide 37: Fundamental period and peak demand
Method | T1
Empirical 1 (storeys) | 0.3 s
Empirical 2 (height) | 0.31 s
Rayleigh simplified | ?
Similar stone buildings [1] | 0.17-0.43 s
Numerical, SAMUEL | 0.305 s
Limit state | E_d Soil A [mm] | E_d Soil E [mm]
No Collapse | 13.61 | 19.05
Significant damage | 13.61 | 19.05
Damage limitation (elastic spectrum) | 6.80 | 9.53
[1] A. Elmenshawi et al. 2010

## Slide 38: Over Strength Ratio
Limit state and capacity
  No Collapse
    Ultimate design capacity C_d
  Significant Damage
    ¾ C_d
  Damage Limitation
    Design peak elastic displacement
    d_peak/CF
Limit state | C_d [mm] | OSR Soil A | OSR Soil E
No Collapse | 58.00 | 4.26 | 3.04
Significant Damage | 43.50 | 3.20 | 2.28
Damage Limitation | 27.41 | 4.03 | 2.88

## Slide 39: Assessment and recommendations
OSR stays way above the 1.0 limit
Remember conditions to be checked for capacity design
  e.g. detailing, material, in-situ loads distribution etc.
If conditions are not met
  Repair and strengthening –specially ground floor (e.g. following Eurocode 8-3 Annex C5)
    Sealing/Grouting of eventual small cracks
    Cross bonded stones at wall intersections (e.g. RC belts, Steel plates/Meshes)
    Strengthening and stiffening of the timber floors
      e.g. double diagonal steel-ties mesh anchored to the perimeter walls
    Anchoring and bracing of roof trusses to the supporting walls. Horizontal bracing should be added to the bottom chords if nonexistent
    Strengthen the overall behavior by adding steel ties (or tie beams) between walls
Adjacent unit effect should be analyzed

## Slide 40: 7. Building models database
Context
Relational database (user POV)
  With interoperability
  No interoperability
Stockage of digital data
  Local machine
  Local server
  Cloud-based

## Slide 41: Building models database context
EESD lab
  Spatial building models to numerically study earthquake behavior
Advances in BIM technology
  Opportunity
Current obstacle
  Interoperability (IfcOpenShell)
@Shebini, 1985

## Slide 42: Relational database (user POV)
Interoperability
No interoperability

## Slide 43: Stockage of digital data
Local machine
  Bad for teamwork (e-mail exchanges not optimal)
  Bad for conservation and changes traceability
Local server
  Most used in AEC industry (organization network)
Cloud-based open solutions
  Opensource solutions like github
  Development idea: Community driven website like grabcad.com

## Slide 44: 8. Next steps
Simplified force-based checks (excel worksheets)
  Magnitude order check
Comparison with other numerical solutions
  Easy since BIM model already exists
Dynamic analysis
  To get vulnerability functions
  Damping & inertial effects (e.g. force distribution) intrinsically considered
Analyze adjacent unit effect on model results
Accidental eccentricities effect
Make the workflow fully reproducible
  Through python code posted on Renku

## Slide 45: Thanks
Professor Katrin Beyer for the project opportunity
T.A. Ivana Bozulic for her precious help

## Slide 46: Quick ULS (linear) mechanism check(FE-Robot)
Not same model (Same wall elastic properties + secondary walls + C20 joists)
Same direction
Same sense
Similar ULS displacement (87 mm, CQC)